# Microcontroller ↔ Touch display API

The 4D touch display connects to the rp2040 (Pico) microcontroller by serial interface.

# Command : servo
## Target : rp2040 Microcontroller
## Description : Move a servo motor
## Command format :
servo	port / P1	command / P2	motor / P3	angle / P4	[speed] / P5

## Parameters :
### P1 Define source task of command
Specifies the return route of the command response. Will allow multiple tasks to send commands and for the responses to get back to the correct source.
Software not implemented as yet, therefore use any value from 0->63
### P2 Command that can be executed by the RP2040 microcontroller
Command list
Command	Code	Notes
ABS_MOVE	0	Move servo to an absolute +/-position
ABS_MOVE_SYNC	1	Set ABS_MOVE command, but wait for a RUN_SYNC_MOVES command to execute
SPEED_MOVE	2	Move servo at a set speed
SPEED_MOVE_SYNC	3	Set SPEED_MOVE command, but wait for a RUN_SYNC_MOVES command to execute
RUN_SYNC_MOVES	4	Run ALL pending SYNC commands
T_DELAY	5	Delay a number of milliseconds
STOP	6	Stop current servo move
STOP_ALL	7	Stop ALL servo moves
ENABLE	8	Enable/disable specified servo

### P3 Motor code
Motor list
Motor	Code	Range (degrees)	Notes
Right_EYE_left/right	0	+/-25	-25=fully left; +25=fully right
Right_EYE_up/down	1	+/-45	-45=fully UP; +45=fully DOWN
Right_EYE_lid	2	+/-25	-25=fully CLOSED; +25=fully OPEN
Right_EYE_brow	3	+/-40	-40=angle UP; +40=angle DOWN
Left_EYE_left/right	4	+/-25	-25=fully left; +25=fully right
Left_EYE_up/down	5	+/-45	-45=fully UP; +45=fully DOWN
Left_EYE_lid	6	+/-25	-25=fully CLOSED; +25=fully OPEN
Left_EYE_brow	7	+/-40	-40=angle UP; +40=angle DOWN
Mouth	8	0 -> +45	0 = mouth OFF, +45 = mouth ON

### P4 Servo angle value
Absolute angle specified in degrees
Microcontroller will check that angle is within mechanical limits
### P5 Servo speed value (optional)
- Only used in TIMED_MOVE command
- Timed value is in units of 100mS

## Returned

Port / (int)	Status / (int)

- Status value : signed integer
- Statue/Errors codes
Error	Code	Notes
OK		Success
BAD_PORT_NUMBER	-104	Port out with range 0 to 63
BAD_NOS_PARAMETERS	-105	Incorrect number of parameters
BAD_BASE_PARAMETER	-106
PARAMETER_OUTWITH_LIMITS	-107	A parameter is out with set limits
BAD_SERVO_COMMAND	-108	Unrecognised servo command

# Command : stepper
## Target : rp2040 Microcontroller
## Description : Move a stepper motor
## Command format :

stepper	port / P1	command / P2	motor / P3	angle / P4

## Parameters :
### P1 Define source task of command
Specifies the return route of the command response. Will allow multiple tasks to send commands and for the responses to get back to the correct source.
Software not implemented as yet, therefore use any value from 0->63
### P2 Command that can be executed by the RP2040 microcontroller
Command list
Command	Code	Notes
SM_REL_MOVE	0	Move steps from current position
SM_ABS_MOVE	1	Move to step value from origin position
SM_REL_MOVE_SYNC	2	Set SM_REL_MOVE command, but wait for a servo RUN_SYNC_MOVES command to execute
SM_ABS_MOVE_SYNC	3	Set SM_ABS_MOVE command, but wait for a servo RUN_SYNC_MOVES command to execute
SM_CALIBRATE	4	Run motor calibrate process / Run motor to maximum point and stop when limit switch is detected / Run motor to minimum point and stop when limit switch is detected / Update limit values and run motor to central position

### P3 Motor
“Pi the Robot” has only a single stepper motor (head rotation), therefore the only legal value is 0.

### P4 angle
- Limited to +/-60 degrees.
- Angle is converted to steps and checked to ensure the move is within limits
  - Very important for relative moves

## Returned

Port / (int)	Status / (int)

Status/Errors codes
Error	Code	Notes
OK	0	Sucess
LETTER_ERROR	-100	Parse cmd : Letter in a number
DOT_ERROR	-102	Parse cmd : extra point in real value
PLUSMINUS_ERROR	-103	Parse cmd : +,- symbol error
QUOTE_ERROR	-131	Parse cmd : quote symbol (“) error

BAD_PORT_NUMBER	-104	Port out with range 0 to 63
BAD_NOS_PARAMETERS	-105	Incorrect number of parameters
PARAMETER_OUTWITH_LIMITS	-107	A parameter is out with set limits
STEPPER_CALIBRATE_FAIL	-109
BAD_STEPPER_COMMAND	-110
BAD_STEP_VALUE	-111
MOVE_ON_UNCALIBRATED_MOTOR	-112
EXISTING_FAULT_WITH_MOTOR	-113
SM_MOVE_TOO_SMALL	-114
LIMIT_SWITCH_ERROR	-115
UNKNOWN_STEPPER_MOTOR_STATE	-116
STEPPER_BUSY	-117

# Command : display
## Target : rp2040 Microcontroller
## Description : Interact with touch screen
## Notes :
There are two types of display command ; API and HIGH LEVEL. There are four API commands that map to the four relevant commands understood by the physical hardware. These use a ‘global index’ access pointer to specify the object.and should not (in most circumstances) be used the high level control software. Users should use the HIGH LEVEL commands to access display hardware. .. One of the main differences is that these HIGH LEVEL command use a ‘local index (see Note 2) to access screen objects. Also they are more descriptive of what effect you want to achieve.

High l(see Note 2) level commands use ‘local index’ to access screen objects. ‘local index’ has a value of 0 to ‘n’ for each form. For example, the first winbutton screen object of a form will have a ‘local index’ value of 0. The microcontroller connected to the display will convert the ‘local index’ value to a ‘global index’ value that is need to access the object on the display hardware.
## High level commands
## Command format :
display	port / P1	command / P2	value_1 / P3	value_2 / P4

display port command form local_index param1 … paramN
Sub-command	Notes	Value
display	Specify a command to interact with the system LCD touch screen
port	Specifies the return route of the command response. Will allow multiple tasks to send commands and for the responses to get back to the correct source.	0 -> 63 / (use 0)
command	Sub-command understood by the RP2040 microcontroller / ()	refer to sub-command list
form	Screen form	0 -> MAX_FORM
local_index		0 -> MAX_INDEX
param1
paramN

## Display sub-commands – ASCII string
Port (1)	Display sub-command code
P[1]	P[2] (2)	Code	P[3]	P[4]	P[5]	Nos parameters (3)
0	SET_uLCD_FORM	0	form	-------	-------	4
0	GET_uLCD_FORM	1	-------	-------	-------	3
0	SET_uLCD_CONTRAST	2	Contrast value	-------	-------	4
0	READ_uLCD_BUTTON	3	form	local index	-------	5
0	READ_uLCD_SWITCH	4	form	local index	source (8)	6
0	READ_uLCD_OBJECT (7)	5	Object type	global index		5
0	WRITE_uLCD_STRING	6	form	local index	string (4)	6
0	WRITE_uLCD_OBJECT (7)	7	Object type	global index	value (5)	6
0	SCAN_uLCD_FORM_BUTTON_PRESSES (6)	8	form	-------	-------	4
0	SCAN_uLCD_SWITCHES (9)	9	form	-------	------	4

Notes
1. The ‘port’ parameter allows the reply from a command to be directed to the task that initiated the command. Not implemented at present so set port parameter to zero.
2. P[n] refers to the nth parameter. Parameter P[0] is the ‘display’ command string
3. Total number of items in a command equals the number of parameters plus the initial ‘display’ ( P[0] ) command
4. ASCII string terminated by a NEWLINE (‘\n’) character
5. 16-bit value
6. Scans the buttons on the active form. Returns the local index of the first button it finds that has a PRESSED state. The command is terminated at this point. Returns a value of -1 if no pressed button is detected.
7. Provide raw access to the READ/WRITE command of the display. These only require the object type and the global index. No reference is made to the form.
8. source = 0 : Read switch from display; source = 1 : read from in memory form_data structure
9. Read all switches on a form. Data is returned as a series of bits in a 16-bit value

## Values returned from display sub-commands – ASCII string
Display sub-command (1)	P[0]	P[1]	P[2]	P[3]	P[4]	Nos parameters
SET_uLCD_FORM	port	status	-------	-------	-------	2
GET_uLCD_FORM	port	status	form	-------	-------	3
SET_uLCD_CONTRAST	port	status	-------	-------	-------	2
READ_uLCD_BUTTON	port	status	value	state (2)	press length (3)	5
READ_uLCD_SWITCH	port	status	value	-------	-------	2
READ_uLCD_OBJECT	port	status	------	------	-------	2
WRITE_uLCD_STRING	port	status	------	------	-------	2
WRITE_uLCD_OBJECT	port	status	------	------	-------	2
SCAN_uLCD_FOR_PRESSED_BUTTON	port	status	local index	press length	-------	4
SCAN_uLCD_SWITCHES	port	status	value (4)			3

Notes
1. All returned values are integer values.
2. state is either PRESSED or NOT_PRESSED
3. press length is in units of 100mS
4. 16-bit value that encodes the binary values of the switches scanned

Status error codes
Error	Code	Notes
OK	0	Sucess
LETTER_ERROR	-100	Parse cmd : Letter in a number
DOT_ERROR	-102	Parse cmd : extra point in real value
PLUSMINUS_ERROR	-103	Parse cmd : +,- symbol error
QUOTE_ERROR	-131	Parse cmd : quote symbol (“) error

GEN4_uLCD_NOT_DETECTED	-119
GEN4_uLCD_WRITE_OBJ_FAIL	-120
GEN4_uLCD_WRITE_OBJ_TIMEOUT	-121
GEN4_uLCD_WRITE_CONTRAST_FAIL	-122
GEN4_uLCD_WRITE_CONTRAST_TIMEOUT	-123
GEN4_uLCD_READ_OBJ_FAIL	-124
GEN4_uLCD_READ_OBJ_TIMEOUT	-125
GEN4_uLCD_CMD_BAD_FORM_INDEX	-126
GEN4_uLCD_WRITE_STR_TOO_BIG	-127
GEN4_uLCD_WRITE_STRING_FAIL	-128
GEN4_uLCD_WRITE_STRING_TIMEOUT	-129
GEN4_uLCD_BUTTON_FORM_INACTIVE	-130

# Command : ping
## Target : rp2040 Microcontroller
## Description : check microcontroller is responding
## Command format :

ping	port / P1	ping value / P2

## Parameters :
### P1 Define source task of command
Specifies the return route of the command response. Will allow multiple tasks to send commands and for the responses to get back to the correct source.
Software not implemented as yet, therefore use any value from 0->63
### P2 Ping value
- Positive integer value sent
- If all is well, ping command will return the value sent plus 1

## Returned

Port / (int)	Status / (int)	Ping value + 1 / (int)

Status/error codes
Error	Code	Notes
OK	0	Sucess
LETTER_ERROR	-100	Parse cmd : Letter in a number
DOT_ERROR	-102	Parse cmd : extra point in real value
PLUSMINUS_ERROR	-103	Parse cmd : +,- symbol error
QUOTE_ERROR	-131	Parse cmd : quote symbol (“) error

# Command : speak
## Target : PC, Rasp-Pi
## Description : Output TTS string

## Command format :

speak

t
f

w
c

“text”
“filename”
P1
P2
P3

## Parameters :
### P1 Define source of text to be spoken
- t = text is part of the command
  - quoted string as parameter 3 (P3)
- f = text in a file
  - quoted filename as parameter 3 (P3)
### P2 Define action when text is spoken
- w = return from command after speech is complete
- c = return from command when speech start

## Returned
Status/error codes
Error	Code	Notes
OK	0	Sucess
TEXTFILE_NOT_FOUND	-100	Parse cmd : Letter in a number

# Command : neopixel
## Target : rp2040 Microcontroller
## Description : Control string of Neopixel RGB LEDS
## Command format :
neopixel	port / P1	command / P2	[par1] / P3	[par2] / P4	[par3] / P5	[par4] / P6

## Parameters :
### P1 Define source task of command
Specifies the return route of the command response. Will allow multiple tasks to send commands and for the responses to get back to the correct source.
Software not implemented as yet, therefore use any value from 0->63
### P2 Command that can be executed by the RP2040 microcontroller
Command list
Command	Code	Notes
NP_SET_PIXEL_ON	0	Set pixel to its ON colour
NP_SET_PIXEL_OFF	1	Set pixel to its OFF colour
NP_SET_PIXEL_FLASH	2	Set pixel to flashing between two colours
NP_BLANK_ALL	3	Set ALL pixels to OFF (BLACK)

### P3-P6 Command parameters
Command	P3	P4	P5	P6	Notes
NP_SET_PIXEL_ON	colour	N/A	N/A	N/A	a
NP_SET_PIXEL_OFF	colour	N/A	N/A	N/A	a
NP_SET_PIXEL_FLASH	on-colour	on-time	off-colour	off-time	a,b
NP_BLANK_ALL	N/A	N/A	N/A	N/A	-

### Notes
The system is set to understand the RAINBOW colours.
Colour	Code	Name	R-value	G-value	B-value
White	0	N_BLACK	0xFF	0xFF	0xFF
Red	1	N_RED	0xFF	0x00	0x00
Orange	2	N_ORANGE	0xFF	0x7F	0x00
Yellow	3	N_YELLOW	0xFF	0xFF	0x00
Green	4	N_GREEN	0x00	0xFF	0x00
Blue	5	N_BLUE	0x00	0x00	0xFF
Indigo	6	N_INDIGO	0x4B	0x00	0x82
Violet	7	N_VIOLET	0x94	0x00	0xD3
Black	8	N_BLACK	0x00	0x00	0x00

Times are set in units of 10mS.